## Slide 1: Porous pavements, green roofs, bioretention. . . Case studies of urban retrofit GI measures funded by Onondaga County’s Green Improvement Fund
Growing Green Infrastructure in New York State and Central New York
November 17-18, 2010
Crown Plaza Hotel, Syracuse New York

## Slide 2: Overview
Onondaga County’s Green Improvement Fund (GIF)
Experience to Date with the Program
Applicants
Approaches
Case Studies
Conclusions

## Slide 3: Onondaga County’s GIF
Announced in Spring of 2010
Funds 100% of GI for sites in eligible CSO districts
Private commercial and non-profits
Application process – ongov.net
Aside from retroactive awards, first projects initiated in Summer 2010

## Slide 4: Experience to Date
NSE has submitted twelve applications to date
Green roofs, porous pavements, bioretention, rain gardens, rainwater harvesting systems
Currently working on five projects

## Slide 5: Wide Variety of Applicants
Range of knowledge of GI
Sometimes with a concept, often times not

## Slide 6: Approach to applications
Owner’s capital needs and designs on site
  Economies between desired improvements and GI.
Site characteristics/constraints
  Structural (green roofs)
  Infiltration
  Soils
  Frost-susceptibility
  Compaction

## Slide 7: Case Studies

## Slide 8: Monroe Building Green Roof
Applicant approached NSE for green roof
Zero lot line
One option. . .
Preliminary evaluation suggested structural adequacy

## Slide 9: Monroe Building Green Roof (cont’d)
Source: Bing Maps

## Slide 10: Monroe Building Green Roof (cont’d)
Conceptual plan
  Root barrier
  Drainage layer
  5 in engineered soil
  vegetation

## Slide 11: Monroe Building Green Roof (cont’d)
Design:
  Structural analysis
    N-S purlin beams structurally adequate
    E-W main girder beams would be overloaded 10-30%
  Currently evaluating lighter system, possibly combined with detention system

## Slide 12: Dunbar Center:

## Slide 13: Dunbar Center (cont’d):
ASLF previously active with GI concepts for site
Infrastructure needs drove GIF application
  Led to conceptual plan for porous surfaces

## Slide 14: Dunbar Center (cont’d):
Design-phase data collection found:
  High infiltration
  Frost-susceptible subgrade soils
Refine conceptual design

## Slide 15: Dunbar Center (cont’d):

## Slide 20
Design Highlights
  Deep infiltration basin
  Impervious asphalt lot and impervious concrete sidewalks
  Roof leader connected to system

## Slide 21: Barada Apartments:

## Slide 22: Barada Apartments (cont’d)

## Slide 23: Barada Apartments (cont’d):
Construction initiated week of 11-15-10

## Slide 24: Conclusions
Start with conceptual based on preliminary site evaluation and owner’s objectives
Collect data
  Structural
  Infiltration
  Etc. . .
Refine concept and initiate design

## Slide 25: Questions?

## Slide 26: Contact:
Kyle E. Thomas, P.E., LEED® APBD+C
Natural Systems Engineering, PLLC
248 Bryant Ave.
Syracuse, New York 13204
kthomas@naturalsystemsengineering.com
www.naturalsystemsengineering.com